## Slide 1
Potential of neural network triggers for the Water-Cherenkov detector array of the Pierre Auger Observatory
Paul Filip – Karlsruhe / Buenos Aires Meeting 14.07.23

## Slide 2: Strategy
  Feed labelled subset of trace to neural network architecture
  Teach it to distinguish between Signal / Background

## Slide 3: Training / Validation data
  QGSJET-II.04 protons with
  UUB Simulation to determine WCD detector response
  Background electronic noise measured in field ( = Random traces)
  Baseline subtraction + Calibration to (true)
  Add both components together to make realistic WCD trace
  See previous Ka/BsAs contributions for details [ 1 / 2 ]
  Full dataset (hopefully) soon accesible publicly for other uses

## Slide 4: Trigger performance
  Classical triggers (Th, ToT, ...) ~100% efficient at in simulations
    Calculated by running full (Offline) simulation chain
    Time consuming approach for prototyping new triggers
  Use Bayesian folding to cut down simulation time
    Assume on station level
    Assume factorizes at event level
    Test assumptions with classical triggers

## Slide 5: Bayesian folding
  lateral trigger probability
    Characterizes chance of trigger w.r.t SPD, Zenith, Energy, etc.
  lateral particle prob.
    Tied to lateral distribution func.
    Ratio of stations that are hit

## Slide 6: Lateral particle probability

## Slide 7: Bayesian folding
  lateral trigger probability
    Characterizes chance of trigger w.r.t SPD, Zenith, Energy, etc.
  lateral particle prob.
    Tied to lateral distribution func.
    Ratio of stations that are hit
  Independent calculation of
    Optimize to specific use-case
    Utilize powerful libraries

## Slide 8
  Threshold trigger (Th)

## Slide 9
  Time-over-Threshold trigger (ToT)

## Slide 10
  ToT-deconvoluted trigger (ToTd)

## Slide 11
  OR( Th, ToT, ToTd )
  MoPS ignored because integral check makes accurate simulation impossible

## Slide 12: Trigger performance
  Base performance on two considerations
  How many showers do we see?
    conditional trigger efficiency
    for individual station
  How often do we trigger (background events)?
    Analyse performance on random-trace dataset
    Trigger rate must not exceed (Bandwidth limitations)

## Slide 13: Trigger performance – Classical triggers

## Slide 14: Trigger performance – Convolutional NNs
  Opt for 120 bin input size
    Shown to work for ToT, ToTd, MoPS
    Compromise network size and input information
  Motivate network architecture on data structure
    2D convolutional layer recognizes correlation between 3 PMTs
    Dense layer propagates extracted features to binary output
  Evaluate performance after training
    32k training events, 8k validation events

## Slide 15: Convolutional neural networks

## Slide 16: Convolutional neural networks

## Slide 17: Convolutional neural networks

## Slide 18: Convolutional neural networks

## Slide 19: Convolutional neural networks

## Slide 20: Filtering and downsampling
Full bandwidth
Filtered & Downsampled

## Slide 21: Filtering and downsampling
Full bandwidth
Filtered & Downsampled
  Filtering smoothes out spikes
  Signal on average smaller

## Slide 22: Filtering and downsampling
Full bandwidth
Filtered & Downsampled
  3 UUB bins = 1 UB bin
  More information per bin

## Slide 23: Convolutional neural networks

## Slide 24: Trigger performance – Recurrent NNs
  Recurrent neural networks capture temporal data
    Backwards connections make it possible to reevaluate output based on earlier input
  Long-Short-Term-Memory (LSTM) architecture
    12 free trainable parameters per cell
    One cell per PMT = 36 parameters
    Dense layer for binary output
    = 44 (possibly 20?) free params
From https://colah.github.io/posts/2015-08-Understanding-LSTMs/

## Slide 25: Recurrent neural networks

## Slide 26: Recurrent neural networks
  Most drastic gains at high inclinations,
  Possibly higher gains at

## Slide 27: Summary / Outlook
  Test data-driven, machine learning concepts
    Bayesian classifier promising, but needs lots of finetuning
    Neural networks work out of the box but „too efficient“
    Control trigger rate by implementing charge cut
  Convolutional neural networks
    Performance of simple CNN architectures on par with Th-Trigger
    Filtered & downsampled data preferred over full bandwidth input
  LSTM / recurrent neural networks
    First results indicate better performance than ToT
    Large gains in event detection efficiency at high shower angles

## Slide 28: Summary / Outlook
  Lot of work needed until prototyping stage is left
    Presented results stem from simulations only
    No primary distinction, only data from protons considered
    Only one hadronic interaction model (QGSJET-II.04)
  Ground work is completed
    Key assumptions have been tested and verified to hold true
    Analysis chain is implemented and ready to run
    Neural networks show a lot of potential as SD triggers

## Slide 29
Backup

## Slide 30: Residuals – LTP fitfunction

## Slide 31: Efficiency scaling – unscaled

## Slide 32: Efficiency scaling – scaled

## Slide 33: Random traces – Power spectrum

## Slide 34: Trace building

## Slide 35: Muon cut

## Slide 36: Kernel size

## Slide 37: Input size

## Slide 38: T3 efficiency calculation
  Offline approach Bayesian folding

## Slide 39: LSTM permutations

## Slide 40: Network parameters

## Slide 41: Sample headline: Arial 24pt bold
Subline: Arial 20pt bold
Lorem ipsum dolor sit amet, consetetur sadipscing
…
  …
  …
Subline: Arial 20pt bold

## Slide 42: Sample headline: Arial 24pt bold
Subline: Arial 20pt bold
Lorem ipsum dolor sit amet, consetetur sadipscing
…
  …
  …
Subline: Arial 20pt bold

## Slide 43: Sample headline: Arial 24pt bold
Lorem ipsum dolor sit amet, consetetur sadipscing elitr, sed diam nonumy eirmod
  At vero eos et accusam et justo duo dolores et ea rebum. Stet clita kasd gubergren
    No sea takimata sanctus est Lorem ipsum dolor sit amet.
Lorem ipsum dolor sit amet, consetetur sadipscing elitr, sed diam nonumy eirmod tempor invidunt
…
…

## Slide 44: Sample headline: Arial 24pt bold
Subline: Arial 20pt bold
Lorem ipsum dolor sit amet, consetetur sadipscing
…
  …
  …
Subline: Arial 20pt bold
Lorem ipsum dolor sit amet, consetetur sadipscing elitr, sed diam nonumy eirmod tempor invidunt ut labore et dolore magna aliquyam erat, sed diam voluptua.
At vero eos et accusam et justo duo dolores et ea rebum. Stet clita kasd gubergren.

## Slide 45: Sample headline: Arial 24pt bold
Subline: Arial 20pt bold
Lorem ipsum dolor sit amet, consetetur sadipscing
…
  …
  …
Subline: Arial 20pt bold

## Slide 46: Sample headline: Arial 24pt bold

## Slide 47: Sample headline: Arial 24pt bold